## Slide 1: How do we know anything? And how can we know things better? A talk about why measurement matters & the recent redefinition of four SI units Michael de Podesta
King’s College, London
13th November 2019

## Slide 2
Introduction
An Alternative System of Units
The International System of Units: the SI
Details, Details, Details.
Summary
How do we get to know anything?
Notes: 2

## Slide 3
vast
?
?
Measurement is the key to understanding the world around us
imperceptible
familiar
Notes: The perceptible and the imperceptible
  A feather falls onto the shoulder of a man as he gets into a train. Does the train use up more fuel to carry him than if he left the feather at home?
  The tides are affected by the motion of the Moon around the Earth. Are the tides affected by the motion of Jupiter?
  When you jump, does the Earth move?
  Does driving your car to work (or choosing not to) affect the CO2 concentration in the atmosphere?
  Does a fan really cool a room, or heat it up?

## Slide 4
It is measurement that makes science scientific. Not Maths.
Notes: 4

## Slide 6
…of an unknown quantity
with a standard quantity
Measurement is…
Quantitative Comparison
Standard
Unknown
Notes: 6

## Slide 7
Measurement is…
Quantitative Comparison
Standard
Unknown
Grade #1 Copy
Grade #2 Copy
Grade #3 Copy
Time
&
Distance
More Time
&
Distance
Even More Time
&
Distance
Notes: 7
The key point here is that the perfection of a standard quantity represents a limit to how well anything can be measured.
SI represents that limit

## Slide 8
Unknown
Candle
Measurement is…
Quantitative Comparison
Standard
1
2
3
4
5
6
7
8
9
#
0
<
3.14
3.1415
3.141
Notes: 8
The key point here is that the perfection of a standard quantity represents a limit to how well anything can be measured.
SI represents that limit

## Slide 9
World-wide comparison of X
XChina
XUK
XJapan
XNew Zealand
XArgentina
XUSA
XCanada
XEU
XRussia
XNigeria
XIndia
Notes: 9
X is some quantity which we wish to compare – perhaps the size of a component.
If the measurements of X in Australia and Nigeria are both traceable to the SI standard, then they can be meaningfully compared with each other.

## Slide 10
The Base Units of the SI
second
metre
kilogram
candela
mole
ampere
kelvin
Notes: A nice big picture of the SI roundel

## Slide 11: Summary of Introduction
Measurement is at the heart of all science & engineering
If we can measure something then we can begin to:
  Understand it (science)
  Improve it (engineering)
Every culture has a system of measurement
On Earth, the International System of Units – the SI – is the only coherent system of units in use.
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 12
Introduction
An Alternative System of Units
The International System of Units: the SI
Details, Details, Details.
Summary
How do we get to know anything?
Notes: 12

## Slide 13
My System of Units
A standard length
A standard mass
A standard time
Michael
Stephanie
Maxwell
1 Maxwell is the period of a pendulum
with length of 1 Michael
and a spherical mass of 1 Stephanie
measured in Teddington
at 20 degrees Christian
Base Units

## Slide 14
…of an unknown quantity
with a standard quantity
Measurement is…
Quantitative Comparison
Standard
Unknown
Notes: 14

## Slide 15: Multiples
We can create multiples and sub multiples-of these ‘units’.
Create copies of the standard Michael
Re-assemble to make multi-Michaels e.g. a pentaMichael
Michael
Michael
Michael
Michael
Michael
Michael
Michael
Michael
Michael
Notice that the standard Michael does two jobs
It defines what we mean by a Michael – definition
It forms the seed for dissemination of the unit - realisation
Base Units
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 16: Multiples and Sub-Multiples
We can create multiples and sub-multiples of these ‘units’.
Create copies of the standard Michael to make multi-Michaels e.g. a pentaMichael
Create demiMichaels and check
  DemiMichaels are equal to each other
  Add up to one Michael
Mich
Mich
Michael
Michael
Michael
Michael
Michael
Michael
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 17: Now we can make measurements!
Michael
Michael
Michael
Mich
a
e
Unknown Length
2.875 Michaels
Base Units
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 18
Time Multiples
Just count Maxwells
1
2
3
4
5
It took 5 Maxwells for the ball to go up and down
Base Units

## Slide 19
Time Sub Multiples
Or count deciMaxwells
1
2
3
4
5
It took 52 deciMaxwells for the ball to go up and down
Base Units

## Slide 20: Speed
Michael
Michael
Mich
a
e
Length = 2.875 Mic
Time = 1.1 Maxwells
Speed = 2.875/1.1 Michaels per Maxwell
Speed = 2.614 Mic O’Max
Derived Units
The unit of speed is called the
Mic O’Max
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 21: Energy
Michael
Michael
Mich
a
e
Length = 2.875 Mic
Speed = 2.614 Mic O’Max
Derived Units
Mass = 1 Steph
Energy = ½ mass x speed2
Energy = 6.833 Steph Mic Mic O’Max O’Max
The unit of energy is called the
Steph Mic Mic O’Max O’Max
XiaoJuan (晓 娟)
Notes: Xiao means "morning" and Juan means "graceful" or "beautiful". Xiao is 晓 and Juan is 娟。

## Slide 22: My System of Units
Michael
Stephanie
Maxwell
Steph
Mic
Max
Base Units
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 23: Acceleration
a
0.25 Mic
a
a
a
a
a
a
a
a
a
0.25 Mic
0.25 Mic
0.25 Mic
0.25 Mic
0.25 Mic
0.25 Mic
0.25 Mic
0.25 Mic
0.25 Mic
Time (Max) | Velocity (Mic O’Max) | Acceleration (Mic O’Max O’Max)
1.667 | 0.150 | 
0.690 | 0.362 | 0.127
0.530 | 0.472 | 0.159
 |  | 0.143
Acceleration = 0.143 Mic O’Max O’Max
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 24: Force
Pick K = 1
1 Sharmila ≡ 1 Steph Mic O’Max O’Max
So that I can just write F = m a and get the answer directly in Sharmilas
Standard Force
force caused by 1 Stephanie
deflecting a standard spring
by 1 centiMichael
Option#2
Option#1
Newton’s second law: Force is proportional to mass and acceleration
Force = K x mass x acceleration
Stephanie, Michael and Maxwell are base units
Sharmila is a derived unit.
(Its just a special name for
1 Steph Mic O’Max O’Max)
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 25: My System of Units
Michael
Stephanie
Maxwell
Sharmila
Steph
Mic
Max
Andrew
Sharmila
Michael
Michael
Inseok
Mic O’Max
Base & Derived Units
degrees Christian
XiaoJuan (晓 娟)
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 26: What’s WRONG with My System of Units
No one else uses it!
  The units we use are for other people’s convenience, not ours!
The standard Michael or Stephanie could get damaged or change length or weight
  This is a real risk!
The standard Michael and Stephanie
  (a) define the units and
  (b) form the seed for dissemination of the unit system.
  This is a conflict
Standard values are arbitrary.
  The choices are dominated by family history
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 27
Introduction
An Alternative System of Units
The International System of Units: the SI
Details, Details, Details.
Summary
How do we know anything?
Notes: 27

## Slide 28
The Base Units of the SI
second
metre
kilogram
candela
mole
ampere
kelvin
Notes: A nice big picture of the SI roundel

## Slide 29
The SI
second
metre
kilogram
candela
mole
ampere
kelvin
newton
volt
ohm
pascal
tesla
hertz
farad
joule
m/s
V/m
Nm
rad/s
J/K
Ωm
kilo, k
Mega, M
Giga, G
Tera, T
Peta, P
femto, f
pico, p
nano, n
micro, µ
milli, m
Exa, E
atto, a
Base Units
Derived Units
Prefixes
Communication
Torque = 3.7 N m
Notes: A nice big picture of the SI roundel

## Slide 30: What’s RIGHT with the International System of Units
Everyone uses it!
  It is humanity’s universal language of measurement!
But like ‘My System’…
  …its just made up!
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 31: What’s RIGHT with the International System of Units
Everyone uses it!
  It is humanity’s universal language of measurement!
But it is like ‘My System’ in many ways.
Base Units are combined to create complex Derived Units
  And, its just made up! – But by agreement.
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 32: What’s WRONG with the International System of Units
The kilogram could be damaged
  This is a real risk!
The kilogram and the kelvin still conflate definitions and realisations of units
  This is still a conflict – but small in practice.
Standard values are arbitrary – not ‘natural’.
  The choices are dominated by history
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 33
The Base Units of the SI
second
metre
kilogram
candela
mole
ampere
kelvin
New!
Notes: A nice big picture of the SI roundel

## Slide 34
Why?
Re-defining the base units of the SI?
Notes: 34

## Slide 35
…of an unknown quantity
with a standard quantity
Measurement is…
Quantitative Comparison
Standard
Unknown
Could we choose our standards more wisely?
Notes: 35
This is the question behind the re-definition

## Slide 36
SI Base Units and Natural Constants
measure
realise
Unit Definitions
in terms of
Unit Definitions
Natural Constants
Notes: 36
Using the human based standards of the SI, we have measured natural features of the universe that appear to be constant: Natural Constants
Note: The phrase ‘natural constants’ has been carefully chosen. Avoid the use of ‘fundamental’ constants – they are not all fundamental.
Natural Constants appear to be more stable than ANYTHING human made – more later – they appear to be at least one million times more stable than the most stable human artefact – the kilogram.
The idea of the unit re-definitions is to base our system of units on these natural constants.

## Slide 37
Measurement of speed of light improves
Measurement of length improves
Speed of Light
Exactly
299 792 458 m s-1
Speed of Light
in metres per second
299 792 458 ±0.6 m s-1
1970
1980
1990
2000
Second
Exactly 9 192 631 770
periods of 133Cs radiation
Metre
Exactly 1,650,763.73 wavelengths of light
from 86Kr atoms
Metre
The distance travelled by light in exactly second
Second
Exactly 9 192 631 770
periods of 133Cs radiation
Metre Re-defined
Redefining the metre in 1983
Notes: This is the story of the way in which the metre was re-defined in terms of the speed of light in vacuum.
This is the same kind of switch we wish to carry out with the ampere and kilogram.

## Slide 38
SI Base Units and Natural Constants
measure
realise
Unit Definitions
in terms of
Unit Definitions
Natural Constants
Notes: 38
Using the human based standards of the SI, we have measured natural features of the universe that appear to be constant: Natural Constants
Note: The phrase ‘natural constants’ has been carefully chosen. Avoid the use of ‘fundamental’ constants – they are not all fundamental.
Natural Constants appear to be more stable than ANYTHING human made – more later – they appear to be at least one million times more stable than the most stable human artefact – the kilogram.
The idea of the unit re-definitions is to base our system of units on these natural constants.

## Slide 39
The aim of all this ‘measuring’ was to ensure that:
size of the units defined by the new definitions
were indistinguishable from
the size of the unit defined by the previous definitions
SI. The International System of Units
Administered from BIPM
  International Bureau of Weights & Measures
Run by the CIPM
International Committee for Weights & Measures
Agenda set by the CGPM
General Conference on Weights & Measures
Start
Measure
Measure
Measure
Measure
Measure
Measure
Measure
Measure
Measure
STOP!
2019
2018
2017
2016
2015
2014
2013
2012
2011
2010
2008
2009
2007
Resolution 12: CGPM 2007
Recommends laboratories pursue the relevant experiments so that the International Committee can come to a view on whether it may be possible to redefine the kilogram, the ampere, the kelvin, and the mole
DRAFT Resolution A: CGPM 2018
Should decide to make the change from 20th May 2019
Notes: 39
CGPM 13th November to 16th November 2018

## Slide 40
The SI is the system of units in which the following constants have these exact values.
Symbol | Constant | Numerical Value | Unit
 | the unperturbed ground state hyperfine transition frequency of the caesium 133 atom | 9 192 631 770 | Hz
c | the speed of light in vacuum | 299 792 458 | m s-1
h | the Planck constant | 6.626 070 15 × 10−34 | J s
e | the elementary charge | 1.602 176 634 × 10−19 | C
k | the Boltzmann constant | 1.380 649 × 10−23 | J/K
NA | the Avogadro constant | 6.022 140 76 × 1023 | mol-1
Kcd | the luminous efficacy of monochromatic radiation of frequency 540 × 1012 hertz | 683 | lm/W.
Symbol | Constant | Numerical Value | Unit
 | the unperturbed ground state hyperfine transition frequency of the caesium 133 atom | 9 192 631 770 | Hz
c | the speed of light in vacuum | 299 792 458 | m s-1
h | the Planck constant | 6.626 070 15 × 10−34 | J s
e | the elementary charge | 1.602 176 634 × 10−19 | C
k | the Boltzmann constant | 1.380 649 × 10−23 | J/K
NA | the Avogadro constant | 6.022 140 76 × 1023 | mol-1
Kcd | the luminous efficacy of monochromatic radiation of frequency 540 × 1012 hertz | 683 | lm/W.
Notes: 40
This is the question behind the re-definition

## Slide 41
The previous structure of the SI
Base Units
m
s
K
kg
A
mol
cd
m s-1
m s-2
kg m-3
Derived Units
kg m2 s–3 A–1
A s
coulomb, C
volt,V
kg m s-2
newton, N
kg m2 s-2
joule, J
kg m2 s–3
watt, W
Reality
Notes: 41

## Slide 42
The new structure of the SI
Base Units
m
s
K
kg
A
mol
cd
m s-1
m s-2
kg m-3
Derived Units
kg m2 s–3 A–1
volt,V
kg m s-2
newton, N
kg m2 s-2
joule, J
kg m2 s–3
watt, W
Natural Constants
c
kB
h
e
NA
Kcd
Reality
A s
coulomb, C
Units
Notes: 42

## Slide 43
Measurement is…
Quantitative Comparison
Standard
Unknown
Grade #1 Copy
Grade #2 Copy
Grade #3 Copy
Time
&
Distance
More Time
&
Distance
Even More Time
&
Distance
Definition
Realisation
Expected to improve with time
Expected to
remain unchanged
Notes: 43
This harks back to the earlier diagram showing how the constants are ‘abstracted’ and should never change.

## Slide 44: The 2019 changes…
Remove uncertainty from unit definitions.
Ends the use of defining artifacts & materials.
?
Blur the distinction between:
base units
derived units
Provides foundations for future developments
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 45
Introduction
An Alternative System of Units
The International System of Units: the SI
Details, Details, Details.
Summary
How do we get to know anything?
Notes: 45

## Slide 46
Detail#1
The kilogram problem
Notes: 46

## Slide 47
The kilogram is the unit of mass;
it is equal to the mass of the international prototype of the kilogram.
The International Prototype of the Kilogram (The IPK)
Notes: 47

## Slide 48
The IPK doesn’t normally weigh one kilogram
Nettoyage
Chamois leather soaked for 48 hours in a mixture of ethanol and ether.
Rubbed ‘fairly hard’ by hand
Lavage
Steam clean
https://www.bipm.org/utils/common/pdf/monographies-misc/Monographie1990-1-FR.pdf
Notes: https://www.youtube.com/watch?v=VlJSwb4i_uQ

## Slide 49
Has the mass of the IPK changed over time?
1 part in 1010 per year

## Slide 50
How can we replace the IPK?
Bryan Kibble 1939 - 2016
Option#2
Measure gravitational force in terms of electromagnetic forces.
Originally, a Watt Balance, now called a Kibble balance.
Option#1
A recipe for creating artifacts of known mass
The Avogadro Project
Notes: https://www.youtube.com/watch?v=VlJSwb4i_uQ

## Slide 51
The Avogadro Approach
NIST

## Slide 52: Recipe for a kilogram of silicon
1. Dimensions
traceable to the metre
2. X-ray analysis gives
lattice constant
traceable to the metre
4. Silicon atomic mass known from spectroscopy
in terms of h/mSi
(unit m2/s - known without reference to the SI kg) gives mSi = K h
6. Surface layers characterised
28Si
3. Using 1 & 2 we can work out
the number of atoms in the sphere, N
5. From 3 & 4 the mass of the sphere is N mSi

## Slide 53
The Kibble balance
Notes: 53

## Slide 54
N
N
S
The Kibble Balance
X
M
Current Source
When falling…
Electro-magnetic Force on M depends on
Mass of M
Electric Current
Coil Shape
Magnetic Field
When balanced…
Voltmeter
Coil
Interferometer
Combining…
Magnet
Rigid Frame
Voltage Induced depends on
Speed
Coil Shape
Magnetic Field
Mass can be deduced from
A voltage measurement
A current measurement

## Slide 55
N
N
S
The Kibble Balance
X
M
Current Source
When falling…
Electro-magnetic Force on M depends on
Mass of M
Electric Current
Coil Shape
Magnetic Field
When balanced…
Voltmeter
Coil
Interferometer
Combining…
Magnet
Rigid Frame
Voltage Induced depends on
Speed
Coil Shape
Magnetic Field
Mass can be deduced from
A voltage measurement
A current measurement
Maths
No Maths

## Slide 56
N
N
S
The Kibble Balance
X
M
Current Source
When falling…
When balanced…
Voltmeter
Interferometer
Combining…
Magnet
Rigid Frame

## Slide 57
N
N
S
The Kibble Balance
X
M
Current Source
When falling…
When balanced…
Voltmeter
Coil
Interferometer
Combining…
Magnet
Rigid Frame

## Slide 58
The Kibble Equation
Josephson Effect
Ohms Law
Josephson Effect
Quantum Hall Effect
Gravimeter
Interferometer

## Slide 59
The Kibble Equation
Josephson Effect
Ohms Law
Josephson Effect
Quantum Hall Effect
Gravimeter
Interferometer

## Slide 62
Measurement is…Quantitative Comparison
Standard
Unknown
Now
Before May 2019
N
N
S
Phenomenon traceable to h, c and ΔνCs
Notes: 62
Playing this idea out for traceability of mass measurement before and after the redefinition

## Slide 63
Planck Constant
Exactly
6.626 070 150 x 10-34
joule seconds
Planck Constant
6.626 070 150 ±
0.000 000 069
x 10-34 joule seconds
Kilogram
Exactly defined by the
Planck constant
Measurement of Planck constant improves
Measurement of mass improves
1900
2000
2100
2200
Kilogram
Exactly the mass of the
international prototype
of the kilogram
Kilogram Re-defined
Redefining the kilogram
Notes: This is the story of the way in which the metre was re-defined in terms of the speed of light in vacuum.
This is the same kind of switch we wish to carry out with the ampere and kilogram.

## Slide 64
Detail#2
Are the constants really constant?
Notes: 64

## Slide 65
Constancy of Constants
We can check our belief that c, h and e are stable in time
The stability of the can be measured using atomic clocks
  Some oscillations depend on
  Others depend on
If we compare the ratio of the clock frequencies over (say) a year, we can tell if is changing.
is dimensionless
it has the same value in any unit system
Notes: Improved Limit on a Temporal Variation of mp/me from Comparisons of Yb+ and Cs Atomic Clocks
N. Huntemann, B. Lipphardt, Chr. Tamm, V. Gerginov, S. Weyers, and E. Peik
Phys. Rev. Lett. 113, 210802 – Published 17 November 2014
Frequency Ratio of Two Optical Clock Transitions in Yb+171 and Constraints on the Time Variation of Fundamental Constants
R. M. Godun, P. B. R. Nisbet-Jones, J. M. Jones, S. A. King, L. A. M. Johnson, H. S. Margolis, K. Szymaniec, S. N. Lea, K. Bongs, and P. Gill
Phys. Rev. Lett. 113, 210801 – Published 17 November 2014

## Slide 66
2014 Experimental tests of the stability of
−0.7±2.1×10−17 per year
NPL
PTB
−2.0±2.0×10−17 per year
Fundamental constants appear to be at least one million times more stable than the kilogram
Notes: 66
In contrast the kilogram has copies (e.g. copy 7) that have changed by:
~ 50 micrograms in 125 years
4×10−10 per year

## Slide 67
Detail#3
Artifacts vs Abstractions
Notes: 67

## Slide 68: Defining artifacts and materials
Kilogram
  Defined as the exact mass of the International Prototype of the Kilogram
Kelvin
  Defines the temperature of the Triple Point of Water to be exactly 273.16 K
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 69
1. Fill with ‘water’
2. Remove the air
3. Seal
4. Water Vapour fills the space
5. Chill the middle
6. Leave to equilibrate
The triple point
Glass vessel
273.16 K
Liquid Water
Water Vapour
Solid Water
All co-exist in equilibrium
of water
Pure Water
Vienna Mean Standard Ocean Water (VSMOW)
Dissolved glass?
Notes: https://www.youtube.com/watch?v=VlJSwb4i_uQ

## Slide 70: The lesson of history
Avoid using artifacts to define units
  It’s fine to use artifacts to disseminate copies.
Abstraction is our friend
  Using exact constants removes the uncertainty from definitions
?
Notes: Measurement is the quantitative comparison of an unknown object with a standard object

## Slide 71
Introduction
An Alternative System of Units
The International System of Units: the SI
Details, Details, Details.
Summary
How do we get to know anything?
Notes: 71

## Slide 72
The New International System of Units
Notes: Graphical illustration of the way the constants are represented along with the units in the logo.

## Slide 73
…brings the world into focus
Precision Measurement…

## Slide 74: Thank you:
The National Physical Laboratory is operated by NPL Management Ltd, a wholly-owned company of the Department for Business, Energy and Industrial Strategy (BEIS).
michael.depodesta@npl.co.uk

## Slide 75
Detail#3
Electrical Units
Notes: 75

## Slide 76
The previous structure of the SI
Base Units
m
s
K
kg
A
mol
cd
m s-1
m s-2
kg m-3
Derived Units
kg m2 s–3 A–1
A s
coulomb, C
volt, V
kg m s-2
newton, N
kg m2 s-2
joule, J
kg m2 s–3
watt, W
Reality
Hard work to realise volts and ohms
in terms of the base units
kg m2 s–3 A–2
ohm, Ω
Notes: 76

## Slide 77
Mercury
kg m2 s–3 A–1
volt, V
Voltage
Source
V
For d = 1 mm,
~50 volts raises mercury by only 0.01 mm
An experiment to absolutely realise volts

## Slide 78: A history lesson
1960: SI Ampere defined in terms of µ0.
Implies realisations of the ampere must be in terms of magnetic forces.
1962:Josephson Effect
Microwaves with frequency f produce a DC Voltage
1980: Quantum Hall Effect
2-dimensional electron gas
Since 1990
The 1990 estimates of h and e have been used to disseminate electrical standards worldwide.
These values changed slightly on Monday 20th May 2019
Notes:   Since 1984, an array of 20,208 junctions has been used to make 1 Volt.
  https://www1.bipm.org/cc/CCEM/Allowed/29/CCEM-15-06-electrical-units-in-new-SI.pdf

## Slide 79: Most significant change
Drift of a high-quality 10 V Zener reference against Josephson standards
Monday’s sudden ‘jump’
Search ‘BIPM Voltage Redefinition’
Notes:   Since 1984, an array of 20,208 junctions has been used to make 1 Volt.
  https://www1.bipm.org/cc/CCEM/Allowed/29/CCEM-15-06-electrical-units-in-new-SI.pdf

## Slide 80
The new structure of the SI
m
s
K
kg
A
mol
cd
kg m2 s–3 A–1
volt,V
Natural Constants
c
kB
h
e
NA
Kcd
Units
kg m2 s–3 A–2
ohm, Ω
Notes: 80